# National Climatic Data Center

## DATA DOCUMENTATION

### FOR

# DATASET WP-3D NOAA-43 HURRICANE SEASON 2007

# October 7, 2008

#### National Climatic Data Center

# 151 Patton Avenue

# Asheville, NC 28801-5001  USA

# 1. Abstract

NOAA’s Aircraft Operations Center (AOC) maintains and operates two WP-3D aircraft for weather research projects throughout the year. Examples of these projects are hurricanes, thunderstorms, atmospheric chemistry and winter weather missions. Each of these projects consists of a series of individual flights. For instance, during hurricane projects the WP-3D may fly a variety of missions through tropical cyclones.

The real-time flight-level data is collected and written to a digital data tape on the aircraft and afterwards converted to a file for faster processing and archiving. For each archived project, there are multiple directories consisting of individual flights. The data in these flight directories contain real-time measurements obtained from sensors located throughout the aircraft’s interior and exterior. Also included in a flight directory are scanned images of the actual flight manifest, the navigation log and the mission observation log.

2. Element Names and Definitions

A data record contains 220 elements, stored as 16 bit integer words, and must undergo a conversion process to be displayed as engineering units (degrees, millibars, etc). All of the navigation data is stored as two16 bit integer words that can only be discerned through special bit shifting operations. If examination of the navigation data is desired, contact AOC for a copy of the bit shifting software.

The flight-level data file contains measurements at one-second intervals. These include time in UTC (Z), Global Positioning System (GPS) and inertial navigation data, altitudes, and a variety of temperature and pressure observations. Depending on the scientific objectives of a project, instrumentation will either be included or excluded from this list.

NOAA-43 Aircraft N43RF Hurricane Season 2008

Array

Location     Description

-----------------------------------------------------------------------

*

1            Setup      MS Byte - Slow tape ID, LS Byte - Acft #

2            Setup      size of slow tape logical record == 220 words

3-8           Setup      Micro 99 time - yr,mo,da,hr,mn,sc; updated by fast

9-11          Fast       TBG 1 time - hr,min,sec; binary (not BCD)

12-14        Fast       TBG 2 time -same as TBG 1

15-17 GPS_TIME Fast GPS Time of fix- hr, min, sec; same as TBG’s

18-19 GPS_Dat Fast GPS Altitude – MS bit = -102400*32 ft

20-21        Fast        GPS Latitude – MS bit = -PI*4 radians

22-23	       Fast        GPS Longitude – MS bit = -PI*4 radians

24-36                      Spare

37             Fast        GPS Status (Glonass only avail on Novatel)

Bits 15-14:  0-GPS only

1- Glonass only

2- GPS + Glonass

Bits 13-8 # of satellites used

Bits 7-4: GPS Quality Indicator; 0-No Fix, 1-GPS,

2- C/A Diff GPS, 9-WAAS, see Novatel

Reference Manual for other codes

Bits 3-0: Mode: 0 or 1-No Fix, 2-2D, 3-3D

38	 	Fast 	    GPS Time of fix 1/100 and HDOP

MS byte: Time of fix hundredth’s of seconds

LS byte: HDOP *10

39		Fast 	     GPS VDOP/PDOP (Novatel only)

MS byte: VDOP * 10

LS byte: PDOP*10

40		Fast        GPS Std Dev of Lat error in meters*10 (Novatel only)

41		Fast        GPS Std Dev of Lon error in meters*10     “          “

42		Fast	     GPS Std Dev of Alt error in meters*10      “          “

43               Fast	     GPS Undulation (geoid – WGS84 ellipsoid) “          “

44-54                         Spare

55-56          Fast       INE 1 Altitude - MS bit = -102400*32 ft (Blended GPS)

57-58          Fast       INE 1 Latitude - MS bit = -PI*4 radians

59-60          Fast       INE 1 Longitude - MS bit = -PI*4 radians

61-62          Fast       INE 1 North Vel. - MS bit = -1638.4*2 knots

63-64          Fast       INE 1 East Vel. - MS bit = -1638.4*2 knots

65-66          Fast       INE 1 Vert. Speed - MS bit = -2048*2 ft/sec

67-68          Fast       INE 1 Drift Angle - MS bit = -PI*4 radians

69-70          Fast       INE 1 Heading - MS bit = -PI*4 radians

71-72          Fast       INE 1 Pitch Angle - MS bit = -PI*4 radians

73-74          Fast       INE 1 Roll Angle - MS bit = -PI*4 radians

75-76          Fast	    HG9550 Radar Alt – MS bit = -102400*32 ft

77-94          Fast       INE 2 Data (Lat -> Roll Angle) - same as INE 1

95             Fast        HG9550 Radar Alt Data in meters; 1 sec avg

96             Fast       Vert Accel from RINU#1 VS – m/sec2 * 668.3136

97             Fast       Vert Accel from RINU#2 VS – m/sec2 * 668.3136

98             Fast       APN-159 RA synchro data in meters; 1 sec avg

99             Fast       Spare

100  INEflg    Fast       # of INE bursts avg'd this sec; ms byte - INE #1

ls byte - INE #2

101  GPSflg   Fast       GPS & RA burst count;

bit 15: GPS GPGGA burst rcvd

bit 14: GPS GPGSA burst rcvd (Novatel only)

bit 13: GPS GPGST burst rcvd             “

bit 12-7: Spare

bit 6-0 : HG95550#1 RA, # of words avg’d this sec

102  GarFlg   Fast     Spare

103  Dig_Err  Fast       Error flags for Dig. Avg.

104              	   Spare

105  ADCstatus ASSRV      ADC unit status - from ADC slow data burst

106  IAUstatus Fast       IAU unit status - from IAU burst

107  OperSel   Slow       Operator selections:

Bits 15-12: TempSel value

11-8  : NavSel value

7      : VertAlt Selection 0-PA, 1-Selected GA

6-4   : Abs(GAflg value)

3-0   : DewSel value

108            Fast       status from Wing Wiring Junction Box

109            Fast       status from Cloud Physics Station

110            Fast       status from Flight Director Station

111            Fast       spare

112            Fast       event switch data - Nav,Sta1,Sta2,Sta3

113            Fast       event switch data - Nrack,Sta5,C3X,Sta7

114            Fast       event switch data - F/D,Pilot

115            Fast

116            Fast

117            Fast       Formvar count

118            Fast       Formvar speed

119            Fast       Vaisala Cabin Pres in mBar*20; LSB is update flag

120-128     Fast       Optional user serial data

129            Fast       AOC SFMR Slot A Antenna Value (Counts)

130            Fast         “      “        “    “ Warm Cal Load Value (Counts)

131            Fast         "      "        "    “ Cold Cal Load Value (Counts)

132            Fast         Prosensing processed SFMR WS & Error estimate

Bit 0-10 – SFWS*10 in m/s or special flag

0-2045: Surface WS 0.0 – 204.5 m/s

2046: WS 204.6- 300.0 m/s

2047: Error in wind estimate (equiv to 999.9)

Bit 11-15 – Error Estimate*3 in m/s

0-30 is equiv to 0-10 m/s estimated error

133-135     Fast         AOC SFMR Slot B Values – same assignments as Slot A

136            Fast         Prosensing processed Rain Rate and Channel status

Bit 0-9- SFRR*10 in mm/hr, or special flag

0-1021: Rain Rate 0.0-102.1 mm/hr

1022: RR 102.2-300 mm/hr

1023: Error in rain estimate (equiv to 999.9)

Bit 10-15 – Channel status; 1 bit for each freq

Bit 10 Freq 0; 1-valid, 0-freq not used

:

Bit 15: Freq 5;     “            “

137            Fast         SFMR Thermistor and Housekeeping Data – see below

138            Fast         SFMR  Update Status Word

Bit 0-2   - Slot A Freq | 000 – Nothing in Slot

Bit 3-5   - Slot B Freq | 001 – Freq #0 (4.74 GHZ)

| 010 – Freq #1 (5.31 GHZ)

|   :

| 110 – Freq #5 (7.09 GHZ)

Bit 6-8 – ISEC(137) data | 000 –Nothing in loc

| 001 – t0 (counts)

| 010 – t1      “

| 011 – t2      “

| 100 – t3	   “

| 101 – t4     “

| 110 – t5     “

| 111 – Internal Press

|            (if MS bit = 0)

|         or mode (MS byte)

|         and Radiometer

|         Serial # (LS byte)

|         (if MS bit = 1)

Bit 9 – Prosensing computed data received:

1: %R record received this sec, 0: no data

Bit 10 – Prosening computed data status

1: data valid, 0: data not valid

Bits 15-11 – Sea Surf Temp for SFMR – 1 sec delay

00b – Bad or missing

01b – Over Land

02b – <7C (~6C) 	14b – 22.5C 	26b – 28.75C

03b – 8C			15b – 23.5C	27b – 29.25C

04b – 10C			16b – 24.5C	30b – 29.75C

05b – 12C			17b – 25.25C	31b – 30.25C

06b – 14C			20b – 25.75C	32b – 30.75C

07b – 16C			21b – 26.25C	33b – 31.25C

10b – 18C			22b – 26.75C	34b – 31.75C

11b – 19.5C		23b – 27.25C	35b – 32.25C

12b – 20.5C		24b – 27.75C	36b – 32.75C

13b – 21.5C		25b – 28.25C	37b - >33C (~34C)

139            Fast       M99 10 mSec tic when time was read - use for clock

drift tracking

140          J-W Liquid water

141          RMST TOTAL TEMP #1

142          RMST TOTAL TEMP #2

143          spare

144          AP Alpha (attack) Pressure

145          DAP Differential Alpha Pressure

146          BP Beta (slip) Pressure

147          DBP Differential Beta (slip) pressure

148          PSW Rosemount static pressure from wingtip(#1281)

149          PQW Rosemount dynamic pressure from wingtip(#1281)

150          RD  Radiometer Down measures SST (PRT-5)

151          Spare

152          RS  Side (CO2) radiometer temperature

153          Spare

154          Spare

155          Spare

156          RADOME ATTACK PRESSURE

157          RADOME SIDESLIP PRESSURE

158          RADOME DIFF. PRESSURE (RPQ)

159          RADOME IMPACT PRESSURE

160          Total Temp #3 (fast response) Port side

161-163      Spare

164          DEWPOINT #2 (DW2) EDGETECH

165          DEWPOINT #1 (DW1) Buck 1011C

166          Spare

167          Dewpoint #3 TDL

168	        Dewpoint #1 Balance- Buck 1011C

169           Spare

170           WVSS-II

171          King Liquid water

172          PS2 – COPILOT Rosemount 1281

173          PQF1 - COPILOT ROSEMOUNT #1281 (FUSELAGE)

174          PQF2 - COPILOT ROSEMOUNT  1221F(FUSELAGE)

175          TT1 Heater Current

176          TT2 Heater Current

177           LICOR H2O Absorption

178 	        LICOR Enclosure Pressure

179	        LICOR Rate – X

180	        LICOR Rate – Y

181	        LICOR Rate – Z

182	        LICOR Acceleration – X

183	        LICOR Acceleration – Y

184           LICOR Acceleration – Z

185           LICOR Sample Pressure

186 -187   Spare

188          AXBT CHANNEL #1

189          AXBT CHANNEL #2

190          AXBT CHANNEL #3

191-219   Spare

220         Checksum for this second

3. Start Date

# 20080601

4. Stop Date

# 20081201

5. Coverage

a. Southernmost Latitude: 10 N (or S)

b. Northernmost Latitude: 45 N (or S)

c. Westernmost Longitude: -100 W (or E)

d. Easternmost Longitude: -035 W (or E)

6.How to Order Data

# Ask NCDC’s Climate Services about costs of obtaining this dataset.

# Phone 828-271-4800

# Fax     828-271-4876

e-mail- orders@ncdc.noaa.gov

# 7. Archiving Data Centers

# Name : National Climatic Data Center/NCDC

# Address: Federal Building

# 151 Patton Ave.

# Asheville, NC 28801-5001

# Voice Telephone: 828-271-4800

# Name: Aircraft Operations Center

# Address: Science and Engineering Division

# P.O. Box 6829

# Macdill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

# 8. Technical Contact

# Flight Director’s Name: Martin Mayeaux

# Address: Aircraft Operations Center

# P.O. Box 6828

# Macdill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

# 9. Known Uncorrected Problems:

# None

10.Quality Statement:

Disclaimer: This data is the raw flight-level weather data that has not been quality controlled for sensor contamination or other instrument related errors.

# 11. References:

# Merceret, F.J., and Davis, H.W., 1981: The Determination of Navigational and Meteorological Variables Measured by NOAA/RFC WP3D Aircraft.