# National Climatic Data Center

## DATA DOCUMENTATION

### FOR

# DATASET WP-3D NOAA-43 NAME EXPERIMENT 2004

# September 20, 2004

#### National Climatic Data Center

# 151 Patton Avenue

# Asheville, NC 28801-5001  USA

# 1. Abstract

NOAA’s Aircraft Operations Center (AOC) maintains and operates two WP-3D aircraft for weather research projects throughout the year. Examples of these projects are hurricanes, thunderstorms, atmospheric chemistry and winter weather missions. Each of these projects consists of a series of individual flights. For instance, during hurricane projects the WP-3D may fly a variety of missions through tropical cyclones.

The real-time flight-level data is collected and written to a digital data tape on the aircraft and afterwards converted to a file for faster processing and archiving. For each archived project, there are multiple directories consisting of individual flights. The data in these flight directories contain real-time measurements obtained from sensors located throughout the aircraft’s interior and exterior. Also included in a flight directory are scanned images of the actual flight manifest, the navigation log and the mission observation log.

2. Element Names and Definitions

A data record contains 220 elements, stored as 16 bit integer words, and must undergo a conversion process to be displayed as engineering units (degrees, millibars, etc). All of the navigation data is stored as two16 bit integer words that can only be discerned through special bit shifting operations. If examination of the navigation data is desired, contact AOC for a copy of the bit shifting software.

The flight-level data file contains measurements at one-second intervals. These include time in UTC (Z), Global Positioning System (GPS) and inertial navigation data, altitudes, and a variety of temperature and pressure observations. Depending on the scientific objectives of a project, instrumentation will either be included or excluded from this list.

NOAA-43 Aircraft N43RF NAME Experiment 2004

Array

Location     Description

-----------------------------------------------------------------------

*

1            Setup      MS Byte - Slow tape ID, LS Byte - Acft #

2            Setup      size of slow tape logical record == 220 words

3-8           Setup      Micro 99 time - yr,mo,da,hr,mn,sc; updated by fast

9-11          Fast       TBG 1 time - hr,min,sec; binary (not BCD)

12-14        Fast       TBG 2 time -same as TBG 1

15-17        GPS_Time Fast 3M GPS Time of fix - hr,min,sec; same as TBG's

18-19        GPS_Dat  Fast  3M GPS Altitude - MS bit = -102400*32 ft

20-21        Fast       3M GPS Latitude - MS bit = -PI*4 radians

22-23        Fast       3M GPS Longitude - MS bit = -PI*4 radians

24-25        Fast       3M GPS North Vel. - MS bit = -1638.4*2 knots

26-27        Fast       3M GPS East Vel. - MS bit = -1638.4*2 knots

28-29        Fast       3M GPS Vert. Vel. - MS bit = -2048*2 ft/sec

30             Fast       BR2G GPS Data Time; 0 to 36000, lsb = 1/100 sec

31             Fast       BR2G GPS Altitude; +/- 32767, lsb = 1 ft

32-33        Fast       BR2G GPS Latitude; msb = -PI*4 radians

34-35        Fast       BR2G GPS Longitude; msb = -PI*4 radians

36             Fast       BR2G GPS Status and Horiz. Dilution of Precision

bits 15,14: 00 - no position, 01 - uncorrected,

10 - diff corrected, 11 - almanac used

bits 13-8: # of satellites used

ls byte - HDOP 00 to 99

37             Spare

38             Fast       3M GPS North Accel. - MS bit = -128 m/s**2

39             Fast       3M GPS East Accel. - MS bit = -128 m/s**s

40             Fast       3M GPS Vert. Accel. - MS bit = -128 m/s**2

41             Fast       3M GPS Chan 1 Status 1 \ See Rcvr 3M Spec. for

42             Fast       3M GPS Chan 1 Status 2 /  bit assignments

43-50          Fast      3M GPS Chan 2-5 Status - same format as Chan 1

51             Fast       3M GPS Figure of Merit word - See Rcvr 3M spec.

Note: Time FOM from word 64 is in reserved bits

(12,11,5,4 in HP notation; 3,4,10,11 in 3M/DEC)

52             Fast       3M GPS expected horiz. error - LS bit = 1 meter

53             Fast       3M GPS expected vert. error - LS bit = 1 meter

54                          Spare

55-56          Fast       INE 1 Altitude - MS bit = -102400*32 ft

57-58          Fast       INE 1 Latitude - MS bit = -PI*4 radians

59-60          Fast       INE 1 Longitude - MS bit = -PI*4 radians

61-62          Fast       INE 1 North Vel. - MS bit = -1638.4*2 knots

63-64          Fast       INE 1 East Vel. - MS bit = -1638.4*2 knots

65-66          Fast       INE 1 Vert. Speed - MS bit = -2048*2 ft/sec

67-68          Fast       INE 1 Drift Angle - MS bit = -PI*4 radians

69-70          Fast       INE 1 Heading - MS bit = -PI*4 radians

71-72          Fast       INE 1 Pitch Angle - MS bit = -PI*4 radians

73-74          Fast       INE 1 Roll Angle - MS bit = -PI*4 radians

75-94          Fast       INE 2 Data - same as INE 1

95             Fast       APN-232 RA Data in meters; 1 sec avg

96             Fast       Spare; 1 sec avg

97             Fast       Spare; 1 sec avg

98             Fast       APN-159 RA synchro data in meters; 1 sec avg

99             Fast       APN-159 RA parallel encoder data in meters

100  INEflg    Fast       # of INE bursts avg'd this sec; ms byte - INE #1

ls byte - INE #2

101  GPSflg   Fast       GPS & APN232 RA burst count;

bits 15-12: Ashtech BR2G GPS # of bursts

bits 11-8 : Collins 3M GPS # of bursts

bits 7-0  : APN232 RA # of words avg'd this sec

102  GarFlg   Fast       # of ISEC word 96 & 97 samples avg'd this sec;

ms byte - ISEC(96), ls byte - ISEC(97)

103  Dig_Err  Fast       Error flags for Dig. Avg.; bit 0 for APN232, etc.

104              Spare

105  ADCstatus ASSRV      ADC unit status - from ADC slow data burst

106  IAUstatus Fast       IAU unit status - from IAU burst

107  OperSel   Slow       Operator selections: ms nybl - temp probe,

nybl 2 - nav. unit, nybl 3 - Alt. source

ls nybl - dewpoint unit

108            Fast       status from Wing Wiring Junction Box

109            Fast       status from Cloud Physics Station

110            Fast       status from Flight Director Station

111            Fast       spare

112            Fast       event switch data - Nav,Sta1,Sta2,Sta3

113            Fast       event switch data - Nrack,Sta5,C3X,Sta7

114            Fast       event switch data - F/D,Pilot

115            Fast

116            Fast

117            Fast       Formvar count

118            Fast       Formvar speed

119            Fast       Vaisala Cabin Pres in mBar*20; LSB is update flag

120-126     Fast       Optional user serial data

127-128     Fast       Kludge @ Fast3_4 - Prosensing SFWS & SFRR x 10

129            Fast       SFMR Time (sec x 2)

130            Fast       SFMR Brightness Temp #0 (4.74 GHz)

131            Fast         "      "        "  #1 (5.31 GHz)

132            Fast         "      "        "  #2 (5.57 GHz)

133            Fast         "      "        "  #3 (6.02 GHz)

134            Fast         "      "        "  #4 (6.69 GHz)

135            Fast         "      "        "  #5 (7.09 GHz)

136            Fast         "  Thermistor Data; MS Byte - t3 Hot Load

LS Byte - t4 Dicke Load

137            Fast         "  Thermistor & Press; MS Byte - t5 Waveguide Temp

LS Byte - Internal Press

PSI x 10

138            Fast         "  Update Status

Bit 0-1   - Freq 0  |

2-3   - Freq 1  | 00 - No Update

4-5   - Freq 2  | 01 - Normal

6-7   - Freq 3  | 10 - Warm Cal

8-9   - Freq 4  | 11 - Hot Cal

10-11 - Freq 5  |

12    - Thermistors

13    - Pressure

14    - Clock

15    - Prosensing WS & RR - kludge

139            Fast       M99 10 mSec tic when time was read - use for clock

drift tracking

140          J-W Liquid water

141          RMST TOTAL TEMP #1

142          RMST TOTAL TEMP #2

143          Dew Point 1 (DW1)  GENERAL EASTERN

144          AP Alpha (attack) Pressure

145          DAP Differential Alpha Pressure

146          BP Beta (slip) Pressure

147          DBP Differential Beta (slip) pressure

148          PSW Rosemount static pressure from wingtip(#1281)

149          PQW Rosemount dynamic pressure from win#tip(#1281)

150          RD  Radiometer Down measures SST (PRT-5)

151

152          RS  Side (CO2) radiometer temperature

153

154          Vertical Acceleration 2

155          Vertical Acceleration 1

156          RADOME ATTACK PRESSURE

157          RADOME SIDESLIP PRESSURE

158          RADOME DIFF. PRESSURE (RPQ)

159          RADOME IMPACT PRESSURE

160          Total Temp #3 (fast response) Port side

161-163      Spare

164          DEWPOINT #2 (DW2) EDGETECH

165          Spare

166          Spare

167          Dewpoint # 3 TDL

168-169    Spare

170           WVSS-II

171          King Liquid water

172          PSF - COPILOT ROSEMOUNT #1281 (FUSELAGE)

173          PQF1 - COPILOT ROSEMOUNT #1281 (FUSELAGE)

174          PQF2 - COPILOT ROSEMOUNT  1221F(FUSELAGE)

175          TT1 Heater Current

176          TT2 Heater Current

177          LICOR H20 Absortion

178          LICOR H20 Enclosure Pressure

179          LICOR Rate –X

180          LICOR Rate – Y

181          LICOR Rate – Z

182          LICOR Acceleration – X

183          LICOR Acceleration – Y

184          LICOR Acceleration – Z

185          LICOR Sample Pressure

186          Spare

187          Spare

188          AXBT CHANNEL #1

189          AXBT CHANNEL #2

190          AXBT CHANNEL #3

191-203   SPARE

204           SFMR Brightness – B3 4.55 GHz

205           SFMR Brightness – B5 5.64 GHz

206           SFMR Brightness – B7 6.96 GHz

207           SFMR Brightness – B8 7.22 GHz

208           SFMR Brightness – B6 6.34 GHz

209           SFMR Brightness – B4 5.06 GHz

210           SFMR Temp –T8 Rcvr Noise Src

211           SFMR Temp – T7 Rcvr Ref Load

212           SFMR Temp – T6 Antenna Left

213           SFMR Temp – T5 Antenna Right

214-219    Spare

220          Checksum for this second

3. Start Date

# 20040705

4. Stop Date

# 20040805

5. Coverage

a. Southernmost Latitude: 20 N (or S)

b. Northernmost Latitude: 33 N (or S)

c. Westernmost Longitude: -118 W (or E)

d. Easternmost Longitude: -082 W (or E)

6.How to Order Data

# Ask NCDC’s Climate Services about costs of obtaining this dataset.

# Phone 828-271-4800

# Fax     828-271-4876

e-mail- orders@ncdc.noaa.gov

# 7. Archiving Data Centers

# Name : National Climatic Data Center/NCDC

# Address: Federal Building

# 151 Patton Ave.

# Asheville, NC 28801-5001

# Voice Telephone: 828-271-4800

# Name: Aircraft Operations Center

# Address: Science and Engineering Division

# P.O. Box 6829

# Macdill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

# 8. Technical Contact

# Flight Director’s Name: Martin Mayeaux

# Address: Aircraft Operations Center

# P.O. Box 6828

# Macdill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

# 9. Known Uncorrected Problems:

# None

10.Quality Statement:

Disclaimer: This data is the raw flight-level weather data that has not been quality controlled for sensor contamination or other instrument related errors.

# 11. References:

# Merceret, F.J., and Davis, H.W., 1981: The Determination of Navigational and Meteorological Variables Measured by NOAA/RFC WP3D Aircraft.