# National Climatic Data Center

## DATA DOCUMENTATION

### FOR

# G-IV (NOAA-49) HURRICANE SEASON 2005

# May 3, 2006

#### National Climatic Data Center

# 151 Patton Avenue

# Asheville, NC 28801-5001 USA

# 1. Abstract

NOAA’s Aircraft Operations Center (AOC) maintains and operates a Gulfstream-IV jet aircraft for weather research projects throughout the year. Examples of these projects include hurricane surveillance, winter storm operations, and ozone and atmospheric chemistry missions. Each of these projects consists of a series of individual flights.

The real-time flight-level data is collected and written to the hard drive (.ADS file) as well as to a digital audio tape (DAT) on the aircraft. Afterwards, the file or tape is read and processed into a NetCDF format by a software program called NIMBUS created by Chris Webster of UCAR. For each archived project sent to NCDC, there are multiple directories consisting of individual flights. The data in these flight directories contain real-time measurements obtained from sensors located throughout the aircraft. Included in a flight directory are the raw ADS data file and the one hertz NetCDF file.

Due to the complexity of the ADS file, the following documentation is designed to describe the contents of the simpler and more commonly used NetCDF file.

2. Element Names and Definitions

NOAA-49 Aircraft N49RF Hurricane Season 2005

The NetCDF file contains the following measured and derived parameters along with the corresponding definitions.

ACINS 			Aircraft Vertical Acceleration from Inertial One- M/(S^2)

ACINS_PITR		Aircraft Vertical Acceleration from Inertial Two M/(S^2)

ADCAOA 		Air Data Computer Attack Angle from Flight Station (Degree)

ADCBCALT		Air Data Computer Baro Corrected Altitude (Meter)

ADCCAS		Air Data Computer Computed Airspeed (M/S)

ADCMACH		Air Data Computer Mach Number (None)

ADCPALT 		Air Data Computer Pressure Altitude (Mbar)

ADCSAT		Air Data Computer Static Air Temperature (Celsius)

ADCTAS		Air Data Computer True Airspeed (M/S)

ADCTAT		Air Data Computer Total Air Temperature (Celsius)

AKRD1			Attack Angle, Left Side (Degree)

AKRD2			Attack Angle, Right Side (Degree)

ALT			IRS Baro-Inertial Altitude from Inertial One (Meter)

ALT_PITR		IRS Baro-Inertial Altitude from Inertial Two (Meter)

AOCDA		Computed Drift Angle from Inertial One (Degree)

AOCDA_PITR		Computed Drift Angle from Inertial Two (Degree)

AOCTK			Computed Track Angle from Inertial One (Degree)

AOCTK_PITR		Computed Track Angle from Inertial Two (Degree)

AP1			Vertical Differential Pressure, Left (mbar)

AP2			Vertical Differential Pressure, Right (mbar)

AT1			Ambient Temperature, Top Left (Celsius)

AT2			Ambient Temperature, Bottom Right (Celsius)

AT3			Ambient Temperature, Top Right (Celsius)

AT4			Ambient Temperature, Bottom Left (Celsius)

ATTACK		Attack Angle, Reference (Degree)

ATX			Ambient Temperature, Reference (Celsius)

BCRYO			No Title

BP1			Horizontal Differential Pressure, Top (Mbar)

BP2			Horizontal Differential Pressure, Bottom (Mbar)

CRYO			CR-2 Hygrometer (Celsius)

CRYOC			CR-2 Hygrometer, Corrected (Celsius)

DAP1			Raw Dynamic Attack Pressure, Left (Mbar)

DAP2			Raw Dynamic Attack Pressure, Right (Mbar)

DAY			Raw Tape Day Component (none)

DBP1			Raw Dynamic Slip Pressure, Top (Mbar)

DBP2			Raw Dynamic Slip Pressure, Bottom (Mbar)

DIFF1			Difference Utility 1 (none)

DIFF2			Difference Utility 2 (none)

DIFF3			Difference Utility 3 (none)

DPL			Dew/Frost Point Temperature, Left (Celsius)

DPLC			Corrected Dew/Frost Point Temperature, Left (Celsius)

DPR			Dew/Frost Point Temperature, Right (Celsius)

DPRC			Corrected Dew/Frost Point Temperature, Right (Celsius)

DPX			Dew/Frost Point Temperature, Reference- Either Right or Left (Celsius)

DPXC			Corrected Dew/Frost Point Temp, Reference- Either Right or Left (Celsius)

DRFTA			Inertial Drift Angle from Inertial One (Degree)

DRFTA_PITR		Inertial Drift Angle from Inertial Two (Degree)

DVALU			D-Value (HGME-PALT) (Meter)

EDPC			Ambient Water Vapor Pressure, Reference (Mbar)

EVENT_CKP		Event Marker (none)

EVENT_CTL		Event Marker (none)

EVENT_FCL		Event Marker (none)

EVENT_FCR		Event Marker (none)

EVENT_RCL		Event Marker (none)

EVENT_RCR		Event Marker (none)

GDIF1			Collins GPS- IRS#1 Position Difference (Meter)

GDIF2			Collins GPS- IRS#2 Position Difference (Meter)

GHALT-SG1		Honeywell GPS Altitude #1 –MSL (Meter)

GHALT_SG2		Honeywell GPS Altitude #2 –MSL (Meter)

GHGSF_SG1		Honeywell GPS Ground Speed #1 (M/S)

GHGSF_SG2		Honeywell GPS Ground Speed #2 (M/S)

GHHDOP_SG1		Honeywell GPS Horizontal Dilution of Position #1 (none)

GHHDOP_SG2		Honeywell GPS Horizontal Dilution of Position #2 (none)

GHHFOM_SG1		Honeywell GPS Horizontal Figure of Merit

GHHFOM_SG2		Honeywell GPS Horizontal Figure of Merit (Meter)

GHLATF_SG1 		Honeywell GPS Latitude #1, Fine (Degree)

GHLATF_SG2		Honeywell GPS Latitude #2, Fine (Degree)

GHLAT_SG1		Honeywell GPS Latitude #1 (Degree)

GHLAT_SG2		Honeywell GPS Latitude #2 (Degree)

GHLONF_SG1		Honeywell GPS Longitude #1, Fine (Degree)

GHLONF_SG2		Honeywell GPS Longitude #2, Fine (Degree)

GHLON_SG1		Honeywell GPS Longitude #1 (Degree)

GHLON_SG2		Honeywell GPS Longitude #2 (Degree)

GHMSTT_SG1		Honeywell GPS Measurement Status #1 (none)

GHMSTT_SG2		Honeywell GPS Measurement Status #2 (none)

GHSTAT_SG1		Honeywell GPS Status #1 (none)

GHSTAT_SG2 		Honeywell GPS Status #2 (none)

GHUTC_SG1		Honeywell Time #1 (Seconds)

GHUTC_SG2		Honeywell Time #2 (Seconds)

GHVDOP_SG1		Honeywell GPS Vertical Dilution of Position #1 (none)

GHVDOP_SG2		Honeywell GPS Vertical Dilution of Position #2 (none)

GHVEW_SG1		Honeywell GPS Ground Speed Vector, East Component #1 (M/S)

GHVEW_SG2		Honeywell GPS Ground Speed Vector, East Component #2 (M/S)

GHVFOM_SG1		Honeywell GPS Vertical Figure of Merit #1 (Meter)

GHVFOM_SG2		Honeywell GPS Vertical Figure of Merit #2 (Meter)

GHVNS_SG1 		Honeywell GPS Ground Speed Vector, North Component #1 (M/S)

GHVNS_SG2		Honeywell GPS Ground Speed Vector, North Component #2 (M/S)

GHVZI_SG1		Honeywell GPS Computed Aircraft Vertical Velocity #1 (M/S)

GHVZI_SG2		Honeywell GPS Computed Aircraft Vertical Velocity #2 (M/S)

GPALT			Collins GPS Altitude MSL- (M)

GPGALT		Collins GPS Geopotential Altitude (M)

GPGSPD		Collins GPS Ground Speed (M/S)

GPLAT			Collins GPS Latitude (Degree)

GPLON			Collins GPS Longitude (Degree)

GPTIME		Collins GPS Time (Seconds)

GPTTP			Honeywell GPS Time to Waypoint (Seconds)

GPVEW		Collins GPS Ground Speed Vector, East Component (M/S)

GPVNS			Collins GPS Ground Speed Vector, North Component (M/S)

GPVSPD		Collins GPS Computed Aircraft Vertical Velocity (M/S)

GSF 			Inertial Ground Speed from Inertial One (M/S)

GSF_PITR 		Inertial Ground Speed from Inertial Two (M/S)

HGALT			APN-232 Radar Geopotential Altitude (Meter)

HGM232		Geometric (Radar) Altitude APN-232- (Meter)

HGM232S		APN-232 Radar Altitude Status Bit (Meter)

HOUR			Raw Tape Time Component (Second)

IAS			Aircraft Indicated Airspeed (M/S)

IWD			Horizontal Wind Direction (IRS) Inertial One (Degree)

IWD_PITR		Horizontal Wind Direction (IRS) Inertial Two (Degree)

IWS			Horizontal Wind Speed (IRS) Inertial One (M/S)

IWS_PITR		Horizontal Wind Speed (IRS) Inertial Two (M/S)

LAT			Latitude from Inertial One (Degree)

LAT_PITR		Latitude from Inertial Two (Degree)

LON			Longitude from Inertial One (Degree)

LON_PITR		Longitude from Inertial Two (Degree)

MACH			Aircraft Mach Number (none)

MINUTE		Raw Tape Time Component (Second)

MONTH		Raw Tape Month Component (none)

MR			Mixing Ratio, T-Electric (G/Kg)

ONE			Constant Value of One (none)

PALT			NACA Pressure Altitude in Meters (Meter)

PALTF			NACA Pressure Altitude in Feet (Feet)

PCAB			Cabin Pressure (Mbar)

PCRYO			CR-2 Hygrometer Pressure (Mbar)

PITCH			Aircraft Pitch Angle from Inertial One (Degree)

PITCH_PITR		Aircraft Pitch Angle from Inertial Two (Degree)

PS1C			Corrected Static Pressure, Top Fuselage (Mbar)

PS1M			Raw Static Pressure, Top Fuselage (Mbar)

PS2C			Corrected Static Pressure, Bottom Fuselage (Mbar)

PS2M			Raw Static Pressure, Bottom Fuselage (Mbar)

PSX			Raw Static Pressure, Reference (Mbar)

PSXC			Corrected Static Pressure, Reference (Mbar)

QC1C			Corrected Dynamic Pressure, Left (Mbar)

QC1M			Raw Dynamic Pressure, Left (Mbar)

QC2C			Corrected Dynamic Pressure, Right (Mbar)

QC2M			Raw Dynamic Pressure, Right (Mbar)

QCX			Raw Dynamic Pressure, Reference (Mbar)

QCXC			Corrected Dynamic Pressure, Reference (Mbar)

RHODL			Absolute Humidity, T-Electric Left (g/(m^3))

RHODR			Absolute Humidity, T-Electric Right (g/(m^3))

RHUM			Relative Humidity (%)

ROLL			Aircraft Roll Angle from Inertial One (Degree)

ROLL_PITR		Aircraft Roll Angle from Inertial Two (Degree)

SECOND		Raw Tape Time Component (Second)

SSDF1			Sideslip Angle, Differential Pressure, Top (Mbar)

SSDF2			Sideslip Angle, Differential Pressure, Bottom (Mbar)

SSLIP			Sideslip Angle, Reference (Mbar)

SSRD1			Sideslip Angle, Top (Mbar)

SSRD2			Sideslip Angle, Bottom (Mbar)

TAS1			Aircraft True Airspeed #1 (M/S)

TAS2			Aircraft True Airspeed #2 (M/S)

TASHC			Aircraft True Airspeed, Humidity Corrected (M/S)

TASX			Aircraft True Airspeed, Reference (M/S)

THDG			Aircraft True Heading Angle From Inertial One (Degree)

THDG_PITR		Aircraft True Heading Angle From Inertial Two (Degree)

THETA			Potential Temperature (Degree)

THETAE		Equivalent Potential Temperature (Celsius)

THETAV		Virtual Potential Temperature (Celsius)

TKAR			Aircraft Track Angle Rate from Inertial One (Degree/Second)

TKAR_PITR		Aircraft Track Angle Rate from Inertial Two (Degree/Second)

TKAT			Aircraft Track Angle from Inertial One (Degree)

TKAT_PITR		Aircraft Track Angle from Inertial Two (Degree)

TT1			Total Temperature, Left Top (Celsius)

TT2			Total Temperature, Right Bottom (Celsius)

TT3			Total Temperature, Left Bottom (Celsius)

TT4			Total Temperature, Right Top (Celsius)

TTX			Total Temperature, Reference (Celsius)

UI			Wind Vector, East Component (M/S)

UX			Wind Vector, Longitudinal Component (M/S)

VEW			Inertial Ground Speed Vector, East Component from Inertial One (M/S)

VEW_PITR 		Inertial Ground Speed Vector, East Component from Inertial Two (M/S)

VI			Wind Vector, North Component (M/S)

VNS			Inertial Ground Speed Vector, North Component from Inertial One (M/S)

VNS_PITR		Inertial Ground Speed Vector, North Component from Inertial Two (M/S)

VSPD			IRS-Computed Vertical Velocity from Inertial One (M/S)

VSPD_PITR		IRS-Computed Vertical Velocity from Inertial Two (M/S)

VY			Wind Vector, Lateral Component (M/S)

WD			Horizontal Wind Direction (Degree)

WI 			Wind Vector, Vertical Gust Component (M/S)

WP3			Damped Aircraft Vertical Velocity from Inertial One (M/S)

WP3_PITR		Damped Aircraft Vertical Velocity from Inertial Two (M/S)

WS			Horizontal Wind Speed (M/S)

XLATC			GPS-Corrected Inertial Latitude (Degree)

XLONC			GPS-Corrected Inertial Longitude (Degree)

XMACH2		Aircraft Mach Number Squared (none)

XVEWC		GPS-Corrected Inertial Ground Speed Vector, East Component (M/S)

XVNSC			GPS-Corrected Inertial Ground Speed Vector, North Component (M/S)

YEAR			Raw Tape Year Component (none)

ZERO 			Constant Value of Zero (none)

3. Start Date

# 20050501

4. Stop Date

# 20051201

5. Coverage

a. Southernmost Latitude: 10 N (or S)

b. Northernmost Latitude: 35 N (or S)

c. Westernmost Longitude: -100 W (or E)

d. Easternmost Longitude: -40 W (or E)

6.How to Order Data

# Ask NCDC’s Climate Services about costs of obtaining this dataset.

# Phone 828-271-4800

# Fax     828-271-4876

e-mail- orders@ncdc.noaa.gov

# 7. Archiving Data Centers

# Name : National Climatic Data Center/NCDC

# Address: Federal Building

# 151 Patton Ave.

# Asheville, NC 28801-5001

# Voice Telephone: 828-271-4800

# Name: Aircraft Operations Center

# Address: Science and Engineering Division

# P.O. Box 6829

# MacDill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

# 8. Technical Contact

# Flight Director’s Name: Martin Mayeaux, Paul Flaherty, Barry Damiano, Jack Parrish

# Address: Aircraft Operations Center

# P.O. Box 6828

# MacDill AFB, FL 33608-0829

# Voice Telephone: 813-828-3310

# Fax: 813-828-5061

NIMBUS Software to read ADS File

http://www.atd.ucar.edu/atd/instruments/raf/ads

Chris Webster

cjw@ucar.edu

# 9. Known Uncorrected Problems:

# none

10.Quality Statement:

Note: The parameters listed as “Reference”, in the elements and definitions section, represent the best sensor chosen amongst the group of sensors measuring an atmospheric phenomenon. The sensor that is used as the reference value may also be used as input for other parameter derivations.

# 11. References:

# none